## Slide 1: Vers une amélioration de la simulation des débits grâce à des données topographiques et hydrogéologiques à haute résolution
Ana SCHNEIDER
3ème année de thèse à UMR METIS (UPMC)
Encadrantes : Agnès DUCHARNE et Anne JOST

## Slide 2: Land Surface Models and river discharge
Gascoin et al. (2009) added a new groundwater reservoir in CLSM to better represent water transfers.
Vergnes and Decharme (2012) validated this new groundwater scheme based on GRACE TWS and GRDC river discharge data.
Soil moisture has important role on climate, and is connected to water table dynamics (Lo et al., 2010) affecting river flow variability by the total runoff.
Depending on water table depth, groundwater can influence land surface processes (Kollet and Maxwell, 2008).

## Slide 3: ORCHIDEE model – Routing scheme
Qout
gstream = 0.24E-3 d/km
gfast = 3E-3 d/km
gslow = 25E-3 d/km
Reservoir property

## Slide 4: ORCHIDEE model – Time constant (τ)

## Slide 5: ORCHIDEE model – Time constant (τ)
ORCHIDEE’s time constant (τ)
  Flow is given by:
  Depends only on the topography, and a property of reservoir
  gslow was based on Senegal basin calibration and is globally constant (Ngo-Duc et al., 2007)
New time constant (τnew)
  Based on the flow recession equation proposed by Brutsaert (2005)
    Unconfined aquifer, rectangular cross-section, rectangular basin, basin scale, aquifer initially saturated, longterm solution, free surface, flow paralel to the surface
  Depends on effective porosity (ne), drainage density (δ), and effective transmissivity (Te)

## Slide 6: ORCHIDEE model – Time constant (τ)
Groundwater residence time:
  1400 (Marsily, 1995) ~ 1500 years (Jeandel and Mosseri, 2011); ORCHIDEE ~ 65 days
Sensitivity analysis with new formulation:
  Constant τ for slow reservoir (groundwater)
  τ = 1 year; τ = 10 years; τ = 100 years;

## Slide 7: New time constant (τ)
Effective porosity (ne):
  Specific yield values from Johnson (1967) associated with Hartmann and Moosdorf (2012) global lithology data (0.14 – 0.26);
  Total porosity values from Gleeson et al. (2014) global data (GLYMPS)

## Slide 8: New time constant (τ)
Effective porosity (ne):
  Specific yield values from Johnson (1967) associated with Hartmann and Moosdorf (2012) global lithology data (0.14 – 0.26);
  Total porosity values from Gleeson et al. (2014) global data (GLYMPS)

## Slide 9: New time constant (τ)
Effective transmissivity (Te):
  Global permeability (Perm) from Gleeson et al. (2014)
  Hydraulic conductivity
  Brutsaert (2008):
    p = 0.3465 (empiric)
  Gleeson et al. (2014):
    D = 100 m
ρ = 999.97 km/m3
g = 9.81 m/s2
μ = 0.001 kg/m.s
Te (m/d)

## Slide 10: New time constant (τ)
Drainage density (δ):
  Sum of river lengths inside a basin divides by its surface area
  Which river network use?
Reference | Threshold for river network extraction |  |  |  |  |  |  |  |  |  |  | 
Hydro1K | 1000 km2 (1000 pixels) |  |  |  |  |  |  |  |  |  |  | 
HydroSHEDS | 25 km2 for 15 arc-sec (100 pixels) |  |  |  |  |  | 100 km2 for 30 arc-sec (100 pixels) |  |  |  |  | 
CCM1* 250m | 1km2 16 pixels | 3km2 48 pixels | 6km2 96 pixels | 15km2 240 pixels | 20km2 320 pixels | 30km2 480 pixels |  | 35km2 560 pixels | 50km2 800 pixels | 60km2 960 pixels | 80km2 1280 pixels | 50km2 800 pixels
CCM2** 100m | 0.72km2 72 pixels | 0.96km2 96 pixels | 1.28km2 128 pixels | 2.40km2 240 pixels | 3.20km2 320 pixels | 4.80km2 480 pixels |  | 5.60km2 560 pixels | 8.00km2 800 pixels | 9.60km2 960 pixels | 12.80km2 1280 pixels | 8.00km2 800 pixels
Observed Data | Resolution | Year
Australia (AU) | 1:50k – 1:250k | 2012
Brazil (BR) | 1:25k – 1:250k | 2015
France (FR) | 1:50k | 2013
New Zealand (NZ) | 1:50k | 2011
United States (US) | 1:24k*** | 2007
***1:24k – 1:100k in some documents. but not all of them
*Colombo et al. (2007)
**Vogt et al. (2007)
Threshold: upstream drainage area value from which the river network starts

## Slide 11: New time constant (τ)
River network extraction (threshold calibration):
  HydroSHEDS data at 15” (Lehner at al., 2008) – DEM used on slope calculations
  Lithology (Hartmann and Moosdorf, 2012) – all classes
  Total precipitation (WFDEI corrected by GPCC) – sum of rainfall and snowfall
  Flow accumulation and flow directions from HydroSHEDS 15 arc-sec
  Calibration compared with FR and AU observed data
  Evaluation over 7.5’ x 7.5’ grid cells based on drainage density values
Comparison of drainage density values using different threshold values with observed drainage density data to find a best value for:
  Lithology classes
  Lithology classes over different precipitation values
  Lithology classes over different slope regions

## Slide 12: New time constant (τ)
Lithology classes:
  Mt – metamorphic
  Pa – acid plutonic
  Pb – basic plutonic
  Pi – intermediate plutonic
  Py – pyroclastics
  Sc – carbonate sedimentary
  Sm – mixed sedimentary
  Ss – siliclastic sedimenary
  Su – unconsolidated sedimentary
  Va – acid volcanic
  Vb – basic volcanic
  Vi – intermediate volcanic
Slope classes:
  Slope < 1%
  Slope over 5%?
Precipitation classes:
  Arid (Ptot < 250 mm/y)
  Semi-arid (250 ≤ Ptot < 500 mm/y)
  Humid (500 ≤ Ptot < 1000 mm/y)
  Very humid (1000 ≤ Ptot < 1500 mm/y)
  Wet (Ptot ≥ 1500 mm/y)

## Slide 13: New time constant (τ)
  Mt – metamorphic
  Pa – acid plutonic
  Pb – basic plutonic
  Pi – intermediate plutonic
  Py – pyroclastics
  Sc – carbonate sedimentary
  Sm – mixed sedimentary
  Ss – siliclastic sedimenary
  Su – unconsolidated sedimentary
  Va – acid volcanic
  Vb – basic volcanic
  Vi – intermediate volcanic
AU su = 77%
FR su = 10%

## Slide 14: New time constant (τ)
  Arid (Ptot < 250 mm/y)
  Semi-arid (250 ≤ Ptot < 500 mm/y)
  Humid (500 ≤ Ptot < 1000 mm/y)
  Very humid (1000 ≤ Ptot < 1500 mm/y)
  Wet (Ptot ≥ 1500 mm/y)

## Slide 15: New time constant (τ)
AU Slope < 1% = 79%
FR Slope < 1% = 20%
AU Slope < 1% = 79%
FR Slope < 1% = 20%

## Slide 16: New time constant (τ)
Slope (%)
Precipitation classes
Lithology classes

## Slide 17: New time constant (τ)
Slope (%)
Precipitation classes
Lithology classes

## Slide 18: New time constant (τ)
Threshold values:
  Simulation 1: 5 threshold classes (1.00 – 4.00 km2), based only on lithology
  Simulation 2: 7 threshold classes (1.00 – 125.00 km2), based on lithology and precipitation
  Simulation 3: 10 threshold classes (0.50 – 125.00 km2), based on lithology and precipitation
  Simulation 4: 15 threshold classes (0.50 – 250.00 km2) , based on lithology, slope, and precipitation

## Slide 19: New time constant (τ)
δ (km/km2)
Observed
HydroSHEDS 15”
Simulation 1
Simulation 2

## Slide 20: New time constant (τ)
δ (km/km2)
Observed
HydroSHEDS 15”
Simulation 3
Simulation 4

## Slide 21: New time constant (τ)
δ (km/km2)
Observed
HydroSHEDS 15”
Simulation 2
Simulation 1

## Slide 22: New time constant (τ)
δ (km/km2)
Observed
HydroSHEDS 15”
Simulation 3
Simulation 4

## Slide 23: New time constant (τ)
Threshold results:
Drainage density depends on lithology and climate
Slope threshold improved AU results
Simulation 5: evaluation of high slope values
Validation over US, BR and NZ
 | AU |  |  |  | FR |  |  | 
 | Bias | Corr. | R2 | RMSE | Bias | Corr. | R2 | RMSE
Obs x HS30 | 0,25 | -0,03 | 0,001 | 0,51 | 0,57 | 0,19 | 0,04 | 0,67
Obs x HS15 | 0,25 | -0,06 | 0,004 | 0,51 | 0,56 | 0,29 | 0,09 | 0,66
Obs x Sim1 | -0,14 | 0,44 | 0,19 | 0,41 | 0,09 | 0,41 | 0,17 | 0,34
Obs x Sim2 | 0,06 | 0,61 | 0,37 | 0,35 | 0,09 | 0,41 | 0,17 | 0,34
Obs x Sim3 | 0,007 | 0,54 | 0,30 | 0,37 | 0,04 | 0,46 | 0,21 | 0,33
Obs x Sim4 | 0,07 | 0,61 | 0,38 | 0,35 | 0,10 | 0,39 | 0,15 | 0,39