## Slide 1: I-GEM Project Impact of Groundwater in Earth system Models ANR/MoST 2014-2018
Overview of the first results
Agnès Ducharne, Rong-You Chen, et al.
<number>
Advancement meeting of the GEM project
February 29th, 2016

## Slide 2: IGEM overview
Objectives:
Explore the impacts of GW on regional and global climate, and its links to water resources availability, through model analyses
Compare the sensitivity of simulated climate to different GW parametrizations within 3 different climate models
Consolidate the potential of France and Taiwan in the interdisciplinary research field of the global water cycle
<number>

## Slide 3: IGEM overview
Scientific Tasks:
Sensitivity to fixed water table depths (WTD), to identify the patterns of “active WTD”, below which GW do not impact regional climate
Dynamic WTD over the recent period, to assess the potential of realistic GW parametrizations to improve the simulated climate, with a focus on land/atmosphere feedback and the persistence/memory in the Earth system
Dynamic WTD and climate change, with 2 complementary questions:
(1) What is the influence of GW on the climate change trajectory?
(2) What is the impact of climate change on water resources
(including GW)?
Dynamic WTD with withdrawals, which artificially increase soil moisture via irrigation, with potential impacts on climate until water resources get exhausted.
<number>

## Slide 4: Advancement of T1
Off-line runs:
3 LSMs: ORCHIDEE, SURFEX, CLM
Princeton forcing over 1979-2010 (32 years), 3-hourly at 1° resolution, with correction of total precip based on GPCC (B. Decharme)
Reference in the standard configuration + 7 simulations with forced water table depth (WTD) between 10 and 0.5 m
Spin-up to reach equilibrium before starting the analysed simulations
All simulations finished in January 2016, analysis in progress
On-line runs:
Following the AMIP protocol, with spin-up for initialization
Simulations in progress in the three groups…
<number>

## Slide 5: Off-line reference simulations
<number>
 | CLM (CFref) | ORCHIDEE (IFref2) | SURFEX (SFref)
Vegetation map | Based on MODIS (Lawrence and Chase, 2007) | CMIP5 | Based on ECOCLIMAP
Nb. of PFTs (including bare soil) | 17 | 13 | 12
LAI | Prescribed | Computed (STOMATE module) | Prescribed
Soil texture | IGBP soil dataset with 4931 soil units with sand and clay content for each soil layer | 12 USDA classes, based on the map of Reynolds et al. (2000) | HWSD soil database using sand, clay and organic carbon content.
Soil hydraulic properties | Brooks and Corey | Van Genuchten (1980) | Brooks and Corey
Independent soil tiles in one grid-cell | No | Yes: up to 3 | Yes: one independent soil for each PFTs
Vertical discretization | Soil depth =3.4 m, with 10 layers of increasing depth | Soil depth = 2 m, with 22 layers | Over the same grid, soil depth can reach 1 to 12m depending on PFTs and permafrost areas
Separate aquifer? | Yes: conceptual aquifer below the soil | No | No for the reference simulation
Drainage and baseflow | Gravitational drainage to aquifer+ TOPMODEL baseflow + aquifer outflow | Gravitational drainage at soil bottom | Gravitational drainage at soil bottom
ORCHIDEE:
No decrease of  and m with depth; no « smoothing » of oversaturation

## Slide 6
Rodell et al. 2015: Eland = 1. 32 mm/d
Notes: Intercepted evaporation (ECanop), bare soil evaporation (ESoil), vegetation transpiration (TVeg), and snow sublimation (SubSnow) are chosen to compose the evaporation flux. In CLM, SubSnow is included in ESoil, so the snow sublimation is always 0. Three models showed a pretty close results in the control run.
<number>

## Slide 7
Rodell et al. 2015:
Qland = 0.86 mm/d
Notes: <number>

## Slide 8
Notes: <number>

## Slide 9: Sensitivity to WTD
The three LSMs are forced with several WTDs following Campoy et al.
WTD = 10, 8, 5, 3, 2, 1 and 0.5 m
Constant WTDs are achieved owing to an upward water flux, Qforce, opposing ET
SURFEX and CLM include an explicit WG reservoir, with hydraulic connection between WTD and soil if WTD>Dsoil

## Slide 10
Notes: In CLM, the qforce is slightly negative in d05, d08 and d10. One possible reason is that the boundary for calculating the subsurface run off in CLM is in 3.8m. When we fix the water table depth under this line, we will need to “take out” the water which dropped from 3.8m. The qforce in SURFEX for WTD fixed into 8m and 10m are 0.
<number>

## Slide 11
Notes: For both CLM and SURFEX, the subsurface runoff dominate the major run off, while in ORCHIDEE, there are no subsurface runoff, hence surface run off is the only component in this term.
The model configuration in SURFEX is the main reason for the large subsurface runoff. In CLM, the bottom layer is in 3.8m while in SURFEX is 12m. The model configuration makes the subsurface runoff in SURFEX in d005 way larger than in ORCHIDEE (model calculate to 2m only) and in CLM (model calculate to 3.8m only).
<number>

## Slide 12
Notes: The total evaporation decreased when water table depth become lower. ORCHIDEE decreased to its limitation faster than CLM and SURFEX, while the last two models have similar response in total evaporation.
<number>

## Slide 13
Notes: The Leaf Area Index (LAI) varies in ORCHIDEE, which make ORCHIDEE sensitive in transpiration and canopy evaporation.
Total evaporation has two major components, one is the transpiration, another is soil evaporation.
In CLM and SURFEX, the variation of total evaporation comes from soil evaporation. In ORCHIDEE, the variation of total evaporation comes from the transpiration.
<number>

## Slide 14: Spatial patterns based on ORCHIDEE
REF, Qle, pluriannual mean

## Slide 15
Pluri-annual means, WTD (m)
WTD05
WTD1
WTD2
WTD3

## Slide 16
WTD10-REF
WTD8-WTD10
WTD5-WTD8
WTD5-WTD3
Pluri-annual means, Qle (W/m2)
Notes: <number>

## Slide 17
Pluri-annual means, Qle (W/m2)
WTD2-WTD1
WTD3-WTD2
WTD1-WTD05

## Slide 18: Critical WTD
WTDc = the deepest WTD to achieve a significant change in ET
Main questions:
  How does WTDc compare with maps of WTD (Fan et al., 2013) and hydrogeological properties?
  Are there distinct features in soil moisture transition zones, known to be hot-spots of strong land-atmosphere coupling (Koster et al., 2004; Dirmeyer, 2011)?

## Slide 19: How to estimate the WTDc?
WTDc = critical WTD = the deepest WTD to achieve a significant change in ET
Based on derivatives of the ET changes with respect to WTD, which can be seen as measures of how the sensitivity of ET to a unit change in WTD evolves with WTD
WTDc involves choosing a threshold ET sensitivity value, below which we can assume that the ET changes resulting from WTD variations are small
It can be 10 W/m2, or 10% of ET(REF), given that 10% is often taken as the precision of ET measurements (Dirmeyer et al., 2000), or…?

## Slide 20: Principle based on global scale means
For a threshold of 1%, WTDc  1m

## Slide 21
Pluri-annual means, Qle/Qle(REF)/WTD (%/m); threshold = 10%/m
WTD3-WTD2
WTD2-WTD1
WTD1-WTD05
WTD5-WTD3

## Slide 22
Why so many negative values?  for WTD1-WTD05
TVeg
ESoil
ECanop
LAI
+
+
-
-

## Slide 23
Possible explaining factors - LAI
The more arid, the deeper the WTDc

## Slide 24
Possible explaining factors – Aridity factor P/Rn
LAI and aridity are strongly correlated

## Slide 25
Possible explaining factors - Texture
In arid zones, clayish soils exhibit a shallower WTDc

## Slide 26: Future work
Map WTDc patterns for the three LSMs
Compare with maps of WTD (Fan et al., 2013) and hydrogeological properties
Compare with LA coupling strength criteria
Compare off-line and online WTDc
EGU 2016 and GRL paper in prep.
Assess the impact of GW onto the simulated climate (water cycle, circulation, energy budget)

## Slide 27: Thank you for your attention
<number>
Advancement meeting of the GEM project
February 29th, 2016

## Slide 28
Pluri-annual means, Qle/WTD (W/m2/m); threshold = 10 W/m2/m
WTD3-WTD2
WTD2-WTD1
WTD1-WTD05
WTD5-WTD3

## Slide 29: off line simulation
Flux term
Notes: <number>

## Slide 30
Notes: Despite the snow sublimation has different pattern than other component, the values are too small which can be neglected when we consider the total evaporation.
<number>

## Slide 31
Notes: The surface runoff in ORCHIDEE has maximum in July, which is a well known problem in snow melting. CLM and SURFEX have their peak in April, mostly because the snow melts in spring in North Hemisphere.
<number>

## Slide 32
Notes: The latent heat has the same pattern with total evaporation, especially the consistent of lower latent heat flux and lower total evaporation in SURFEX in DJFMA.
<number>

## Slide 33
Notes: Soil evaporation has the same decreased pattern, while ORCHIDEE approach to its limit quicker than other two models.
<number>

## Slide 34
Notes: The canopy evaporation in CLM and SURFEX do not vary a lot, while ORCHIDEE is sensitive to the water table depth.
So is the transpiration. One possible reason is that the LAI (Leaf Area Index) in CLM and SURFEX do not vary.
<number>

## Slide 35
Notes: <number>

## Slide 36
Notes: In CLM, snow sublimation is always 0. In ORCHIDEE and SURFEX, the value did not change a lot, hence the variance can be neglected.
<number>

## Slide 37
Notes: Net Q flux = surface runoff + subsurface runoff – qforce.
Most of the water which fills into soil layer will flow away through surface runoff or subsurface runoff, few of them transfer into soil vapor.
<number>

## Slide 38
CLM
  Qsb = drainage
  Qforce = water added after drainage
SUR
  Qsb = drainage – Qforce
  Qforce = water added after drainage
ORC
  Qsb = 0
  Qforce = water added (no drainage)
Notes: This is the original setting in subsurface runoff and qforce for three models.
<number>

## Slide 39
Notes: Since the energy budget is fixed, the total heat do not vary a lot.
<number>

## Slide 40
Notes: The latent heat has its effect with the total evaporation. The rest of the total heat will transfer into sensible heat.
<number>

## Slide 41
Notes: <number>

## Slide 42: off line simulation
TWS
Notes: <number>

## Slide 43
Notes: Canopy interception (CanopInt), snow depth (SWE), and soil water (SoilMoist) are chosen to be composed the total water storage (TWS). Each component has its own annual range.
<number>

## Slide 44
Notes: <number>

## Slide 45
Notes: Snow water equivalent is pretty similar in different experiment.
<number>

## Slide 46
Notes: The variation of annual range of soil moisture is pretty similar to TWS.
In CLM, the annual range increased, and then decreased, while in ORCHIDEE, the annual range of soil moisture increased to its limit and stay in there. For SURFEX, the annual range is always increased.
<number>

## Slide 47
Notes: TWS has two major components, SWE and SoilMoist. The SWE does not vary a lot, so most of the variance comes from the SoilMoist. One point we need to mentioned about is that although the SoilMoist in ORCHIDEE does not change in d03, d05, d08 and d10, the annual change in TWS are still decreased. Probably because the seasonal cycle does change in ORCHIDEE.
<number>

## Slide 48: Other issue
Notes: Two problems we may need to solve
<number>

## Slide 49
Notes: The soil moisture suggested more spin-up time for ORCHIDEE in d05, d08 and d10. We think the results will not alter the analysis in flux term, and also has limited effectin total water storage.
<number>

## Slide 50
Notes: We found that the seasonal cycle of soil moisture in CLM are quite strange in d01 and d02. Currently, we have no idea about the reason to caused it. We may check it later, but before that, we will stick with the current results.
<number>